## Slide 1
Chassis

## Slide 2
Rules and Limitations

## Slide 3
Rules and Limitations
Driver’s helmet must have a clearance of 6 in to the side surfaces
Driver’s torso, arms, legs, shoulders, hands, hips, thigh, knees and elbows must have a clearance of 3 in to the side surfaces.
Vehicle |  |  | 
Vehicle/Dimensions | Long | Tall (frame) | Width
Rules | 108 in | N/A | 64 in
Z6 | 95 in | 48 in | 64 in
Z7 | 82.5 in | 50 in | 64 in
Z8 | 88 in | 48.5 in | 63.5 in
ZR 2016 | 75.68 in | 45.625 in | 62 in
ZR 2017 | 86.82 in | 46.125 in | 62 in

## Slide 4
 | Outside diameter | Wall thickness
P. Member | 1.25 | .065
S. Member | 1 | .065
S. Member | 1 | .065
S. member | 1 | .065
S. member | 1 | .065
*Secondary members must be steel tubes having a minimum wall thickness of 0.89 mm (.035 in) and a minimum outside diameter of 25.4 mm (1.0 in

## Slide 5
Rules and Limitations

## Slide 6
Rules and Limitations
 | Recommended tubing specification | Designed tubing specification
Modulus of elasticity | E=205 Gpa (29700 ksi) | E=205 Gpa (29700 ksi)
Outer Diameter | Do=25.4 mm | Do=31.75 mm
Thickness | t= 3.05 mm | t= 1.651 mm
Inner Diameter | Di= 19.3mm | Di= 28.448 mm
Are moment of inertia | I= 13620.9 mm^4 | I= 17732.4 mm^4
Yield Strength | Sy= 365MPa (53 000 psi) | Sy= 690MPa (100 264 psi)
Distance to extreme fiber | c=12.7 mm | c=15.875 mm
Bending strength | 3.915e5 N-mm | 7.707e5 N-mm

## Slide 7
Structural Members
RRH: Rear Roll Hoop
RHO: Roll Hoop Overhead Members
FBM: Front Bracing Members
ALC: Aft Lateral Cross Member in Rule B8.3.3
BLC: Overhead Lateral Cross Member
FLC: Front Lateral Cross Member in Rule B8.3.4
CLC: Upper Lateral Cross Member
DLC: SIM Lateral Cross Member
LFS: Lower Frame Side Members
LDB: Lateral Diagonal Bracing
SIM: Side Impact Members
FAB: Fore/Aft Bracing Members
USM: Under Seat Member
RLC: Rear Lateral Cross Member
Any tube that is used to mount the safety belts or fuel tank

## Slide 8
Dimensional Limitations
Rear Roll Hope (RRH) must be at least 29 in wide at a height of 27 in.
Sides can be bent or straight

## Slide 9
Rules Compliance
Vehicle |  |  | 
Vehicle/Dimensions | Long | Tall (frame) | Width
Rules | 108 in | N/A | 64 in
ZR | 85.95 | 46.175 in | 62 in

## Slide 10
Modifications

## Slide 11
Mass = 92.16 pounds
Mass = 81.86 pounds

## Slide 12
ZR 2016
ZR 2017

## Slide 13
ZR 2016
ZR 2017

## Slide 15
Critical Joints
In order to define the critial joints for the Chassis, we must look for the principal objective of this subsystem that is to keep alive the driver.
Critical joints:
  Seat
  Safety belts
  Head restraint
  Steering Wheel
  Firewall
  Rack & pinion (steering)
  Suspensions

## Slide 16
Joints with Other Systems

## Slide 17
Front Suspension
ZR Front Suspension joint.
ZR Front Suspension joint.

## Slide 18
Rear Suspension
ZR Rear Suspension joint with bolt joints.

## Slide 19
Structural Analysis

## Slide 20
Load cases
Case 1: Front impact
Case 2: Front Rollover
Case 3: Side impact
Case 4: Side Rollover
Case 5: Front long impact

## Slide 21
Dynamic Loads

## Slide 22
FEM

## Slide 23
1.25” Diameter 0.065” Thick Tube
Front Suspension Cage
Roll Cage

## Slide 24
1” Diameter 0.065” Thick Tube
Splash Shield or Firewall
Power Train Cage
*Tubos tojos no son tomados en cuenta

## Slide 25
1” Diameter 0.065” Thick Tube
Front and Back Bumpers
Side Support Bars
Motor support Bars
Skid Plate Support

## Slide 26
CHASSIS Load Distribution

## Slide 27
Power Train Load Distribution
RIGID ELEMENT BARS

## Slide 28
REAR AND FRON SUSPENSION LOAD DISTRIBUTION

## Slide 29
REAR SUSPENSION LOAD DISTRIBUTION

## Slide 30
FRONT SUSPENSION LOAD DISTRIBUTION

## Slide 31
SPLASH AND SKID PLATE LOAD DIST

## Slide 32
SEAT-PILOT INTERFACE

## Slide 34
Front Impact
Highest stress concentration 1.56 E+004 PSI.
Welding factor of 1.54
Safety factor of 4.17

## Slide 35
Front Rollover
Maximum combined stress of 3.42 E+004 PSI
Welding factor of 1.54
Factor of safety 1.90.

## Slide 36
Side impact
Maximum combined stress of 4.48 E+003 PSI
Welding factor of 1.54
Factor of safety 14.53.

## Slide 37
Side Rollover
Maximum combined stress of 4.26 E+004 PSI
Welding factor of 1.54
Factor of safety 1.52.

## Slide 38
Front Long Impact
Maximum combined stress of 2.35 E+004 PSI
Welding factor of 1.54
Factor of safety 2.77

## Slide 39
 | Max G’s applied | Yield Strength | Maximum Stress | Safety Factor
Load Case 1 Front Impact | 1.2 | 66 717.35 psi | 15 600 psi | 4.17
Load Case 2 Front rollover | 3.1 | 66 717.35 psi | 34 200 psi | 1.90
Load case 4 Side impact | 1.4 | 66 717.35 psi | 44 800 psi | 14.53
Load Case 3 Side rollover | 3.1 | 66 717.35 psi | 42 600 psi | 1.52
Load case 5 Front long impact | 2.3 | 66 717.35 psi | 23 500 psi | 2.77